## Slide 1: Component locator
12/29/2023
Steve Grey-Wilson

## Slide 2: Component locator summary
The component locator example was originally based on an Automotive use model but could address any experience that uses the construct of a Work package that has work instructions, related models and the visual AR requirement of locating and understanding where and what the instructions are.
The architecture requires a data store for Work package definition, models and model targets. The implementation uses Thingworx Data tables, services and Repo as the physical data store.
Additionally, a Vuforia Experience server and View as the mobile app (This solution has not be designed for Hololens although with some work on the UI it could be possible. )

## Slide 3: Component locator
Experience Server
Work Instructions
Service requests
Model and Targets Repo

## Slide 4: implementation SUMMARY
The components of the Experience are
Barcode or ID to identify the start point (barcode in our case)
A Work Package(s) related to ID
  Each Work Package consists of
    Work Order summary (step 0)
      Work Instruction per step
      Affected Parts(models) per step

## Slide 5: IMPLEMENT DETAILS
Work Instruction
AutoARWorkInstruction_DT
  WorkID (Key) Identifier
  StepNumber (Key)
  Label1
  Label2
  Label3
  StepDetail
  AffectedPartsID (reference ID)
schema
Hero Part Model Target Identifier
AutoARHeroPart_DT
  VIN (key)
  Folder
  MTID
  MTDataset
  MTGuideView
  Model
Related Models in Step
AutoARAffectedParts_DT
  AffectedPartID (Key)
  MetadataID
  MetadataPropertyName
  ModelName
  DisplayName // redundant maybe this can from the metadata
  PartName // redundant maybe this can from the metadata
  FileName
Work Order that binds the VIN and Instructions
AutoARWorkOrder_DT
  WorkID (Key)
  Title
  Overview
  Difficulty
  Time
  VIN

## Slide 6: IMPLEMENT DETAILS
Create Data
let crvVin = "123456789";
CreateHeroPart('Crv' , 'crv_outer360', 'crv_outer360', 'crv_outer_GuideView_0000_2.png', 'crv_outer.pvz' , crvVin);
//
Hero Part Model Target Identifier
AutoARHeroPart_DT
  VIN (key)
  Folder
  MTID
  MTDataset
  MTGuideView
  Model
Pseudo function
The VIN is the Vehicle identifier
The Folder is the repo location for the Targets and Affected Items
The MTID is the identifier used within the XML and the Dataset
The MTDataset is the model target data definition
The MTGuideview is the image silhouette presented to the user
The Model is the pvz model as the target model

## Slide 7: IMPLEMENT DETAILS
schema
Pseudo function
let apDTC_B1028_1 = CreateWi(id,'Please make sure all safety options have been worked through.',1,'Safety');
Work Instruction
AutoARWorkInstruction_DT
  WorkID (key)
  StepNumber (key)
  Label1
  Label2
  Label3
  StepDetail
  AffectedPartsID
Create Data
WorkInstructions are based on WorkID and StepNumber
Label1,2,3 are UI labels that can be populated depending on the requirement on the Instruction (can be blank)
StepDetail provides the detail

## Slide 8: IMPLEMENT DETAILS
Work Order that binds the VIN and Order ID
AutoARWorkOrder_DT
  WorkID
  Title
  Overview
  Difficulty
  Time
  VIN
Pseudo function
createWorkOrder
  WorkID = 'WIB1028’,
  Title ="Rear Window Wiper Motor. As Signal Error" ,
  Overview = "Rear Window Wiper Motor (As) Signal Error : If you are troubleshooting multiple DTCs, be sure to follow the instructions in B-CAN System Diagnosis Test Mode A" ,
  Difficulty = "Medium" ,
  Time = 300,
  VIN = 123456789;
//
Create Data
The Vin defines the vehicle and WorkID’s the actions to be taken

## Slide 9: IMPLEMENT DETAILS
Related Models in Step
AutoARAffectedParts_DT
  AffectedPartID (key)
  MetadataID (key)
  MetadataPropertyName
  ModelName
  DisplayName // redundant maybe this can from the metadata
  PartName // redundant maybe this can from the metadata
  FileName
createAffectedPart(apDTC_B1028_1, "/134", "path", "ap_rear_wiper_motor" , "REAR_WIPER_MOTOR.PRT" , "REAR_WIPER_MOTOR.PRT" , "/Crv/AffectedPart/rear_wiper_motor.pvz" );
createAffectedPart(apDTC_B1028_1, "/68/85/@@PV-AUTO-ID@@010", "path", "tailgate_wireharness" , "BUNDLE_1" , "BUNDLE_1" , "/Crv/AffectedPart/tailgate_wireharness.pvz" );
createAffectedPart(apDTC_B1028_1, ":5/134", "path", "ap_underDashFuseRelayBox" , "UNDERDASHFUSERELAYBOX.PRT" , "UNDERDASHFUSERELAYBOX.PRT" , "/Crv/AffectedPart/underDashFuseRelayBox.pvz" );
createAffectedPart(apDTC_B1028_1, "/138", "path", "ap_gauge_control_unit" , "GAUGE_CONTROL_UNIT.PRT" , "GAUGE_CONTROL_UNIT.PRT" , "/Crv/AffectedPart/gauge_control_unit.pvz" );
Create Data
Pseudo function

## Slide 10: Work PACKAGE as JSON (this could easily be SXSL, currently we don’t have a sxsl generator as the definition is complex and beyond the scope of this POC)
  Title
  Overview
  Difficulty
  Time
  WorkID
  Models
  WorkInstructions {
  "StepNumber": "0.0",
  "Label1": "Work Order: Rear Window Wiper Motor. As Signal Error",
  "Label3": "Time Est.: 1.0",
  "Label2": "Difficulty: Medium",
  "WorkID": "WIB1028",
  "StepDetail": "Overview: Rear Window Wiper Motor (As) Signal Error : If you are troubleshooting multiple DTCs, be sure to follow the instructions in B-CAN System Diagnosis Test Mode A"
  },
  {
  "AffectedPartsID": "3KK4EQN7VU",
  "StepNumber": "1.0",
  "Label1": "Safety",
  "Label2": "",
  "Label3": "",
    "Models": {
    "array": [
    {
    "path": "/134",
    "model": "ap_rear_wiper_motor"
    },
    "PartsList": [
      {
      "ModelName": "ap_rear_wiper_motor",
      "AffectedPartID": "3KK4EQN7VU",
      "FileName": "/Crv/AffectedPart/rear_wiper_motor.pvz",
      "MetadataID": "/134",
      "source": "demo",
      "MetadataPropertyName": "path",
      "tags": [],
      "PartName": "REAR_WIPER_MOTOR.PRT",
      "sourceType": "User",
      "DisplayName": "REAR_WIPER_MOTOR.PRT",
      "location": {
      "latitude": 0,
      "longitude": 0,
      "elevation": 0
      },
      "key": "3KK4EQN7VU/134",
      "timestamp": "2023-12-20T21:19:02.159Z"
},
Subsequenent steps have an array of models and a PartsList
An array of all models used within the WorkPackage – this is a convenience entry
This is an array of steps where step zero is a special case (this may need rework as its really a summary entry point of the instructions)

## Slide 11: IMPLEMENT DETAILS
Service requests
AutoARServiceHelper
GetWorkPackage based on Vin number (could be any ID)
Returns JSON (InfoTable)
  Package of Work Instructions with steps and related Model.
GetHeroData based on Vin number (could be any ID)
Returns
  VIN
  Folder
  MTID
  MTDataset
  MTGuideView
  Model

## Slide 12: IMPLEMENT DETAILS
Model and Targets Repo
Thing:AutoARRepo
Thingworxs repo that holds
Named Folders
Which contain the
Model Target data
And Affected part models
Use the model target generator and place files in a folder

## Slide 13: Demonstration on device

## Slide 14: Installation
The CreoViewRWHelper extension is required to be installed
https://github.com/mvonhasselbach/CreoViewRWExtension/releases
ARAutoEntities.xml entities need to be imported
Create a test folder in the Thing:AutoARRepo
Copy Polaris files to the D:\ThingWorx\ThingworxStorage\repository\AutoARRepo
Run BuildData service from Data Table:AutoARHeroPart_DT